## Slide 1: Michigan Rehabilitation Code for Existing Buildings Plan Review
Program Approval Number: CP-23-00071
Class Title: Class Category: Rules & Acts (formerly Administration) and Plan Review
Registration Category: BI or registrants with ONLY BO/PR, but no inspector registration
Hours Approved: 1 hr Rules & Acts; 3 hrs Plan Review

## Slide 2: Scope
Chapter 1:
1

## Slide 3: 106
106.1 Submittal of documents. Construction documents, special inspection and structural observation programs, investigation and evaluation reports, and other data shall be submitted in 1 or more sets with each application for a permit. The construction documents shall be prepared by or under the direct supervision of a registered design professional when required by 1980 P.A. 299, MCL 339.101 to 339.2721. Where special conditions exist, the building official is authorized to require additional construction documents to be prepared by a registered design professional.
Exception: The building official is authorized to waive the submission of construction documents and other data not required to be prepared by a registered design professional if it is found that the nature of the work applied for is such that reviewing of construction documents is not necessary to obtain compliance with this code.
R 408.30562
CHAPTER 1: SCOPE

## Slide 4: 106
106.3 Examination of documents. The code official shall examine or cause to be examined the submittal documents and shall ascertain by such examinations whether the construction or occupancy indicated and described is in accordance with the requirements of this code and other pertinent laws or ordinances.
CHAPTER 1: SCOPE

## Slide 5: 106
106.3.2 Previous approval. This code shall not require changes in the construction documents, construction or designated occupancy of a structure for which a lawful permit has been issued and the construction of which has been pursued in good faith within 180 days after the effective date of this code and has not been abandoned.
CHAPTER 1: SCOPE

## Slide 6: 106
106.3.3 Phased approval. The code official is authorized to issue a permit for the construction of foundations or any other part of a building before the construction documents for the whole building or structure have been sub- mitted, provided that adequate information and detailed statements have been filed complying with pertinent requirements of this code. The holder of such permit for the foundation or other parts of a building shall proceed at the holder's own risk with the building operation and without assurance that a permit for the entire structure will be granted.
CHAPTER 1: SCOPE

## Slide 7: Definition
Chapter 2:
2

## Slide 8
ADDITION. An extension or increase in floor area, number of stories, or height of a building or structure.
ALTERATION. Any construction or renovation to an existing structure other than a repair or addition. Alterations are classified as Level 1, Level 2 and Level 3.
CHANGE OF OCCUPANCY. A change in the use of the building or a portion of a building. A change of occupancy shall include any change of occupancy classification, any change from one group to another group within an occupancy classification or any change in use within a group for a specific occupancy classification.
EXISTING BUILDING. A building erected prior to the date of adoption of the appropriate code, or one for which a legal building permit has been issued.
CHAPTER 2: DEFINITION

## Slide 9
LOAD-BEARING ELEMENT. Any column, girder, beam, joist, truss, rafter, wall, floor or roof sheathing that supports any vertical load in addition to its own weight or any lateral load.
PRIMARY FUNCTION. A primary function is a major activity for which the facility is intended. Areas that contain a primary function include, but are not limited to, the customer services lobby of a bank, the dining area of a cafeteria, the meeting rooms in a conference center, as well as offices and other work areas in which the activities of the public accommodation or other private entity using the facility are carried out. Mechanical rooms, boiler rooms, supply storage rooms, employee lounges or locker rooms, janitorial closets, entrances, corridors and restrooms are not areas containing a primary function.
REPAIR. The reconstruction or renewal of any part of an existing building for the purpose of its maintenance or to correct damage.
CHAPTER 2: DEFINITION

## Slide 10
UNSAFE. Buildings, structures or equipment that are unsanitary, or that are deficient due to inadequate means of egress facilities, inadequate light and ventilation, or that constitute a fire hazard, or in which the structure or individual structural members meet the definition of “Dangerous,” or that are otherwise dangerous to human life or the public welfare, or that involve illegal or improper occupancy or inadequate maintenance shall be deemed unsafe. A vacant structure that is not secured against entry shall be deemed unsafe.
WORK AREA. That portion or portions of a building consisting of all reconfigured spaces as indicated on the construction documents. Work area excludes other portions of the building where incidental work entailed by the intended work must be performed and portions of the building where work not initially intended by the owner is specifically required by this code.
CHAPTER 2: DEFINITION

## Slide 11: Compliance
Chapter 3:
3

## Slide 12
301.1 General. The repair, alteration, change of occupancy, addition or relocation of all existing buildings shall comply with one of the methods listed in Sections 301.1.1 through 301.1.3 as selected by the applicant. Sections 301.1.1 through 301.1.3 shall not be applied in combination with each other. Where this code requires consideration of the seismic force- resisting system of an existing building subject to repair, alteration, change of occupancy, addition or relocation of existing buildings, the seismic evaluation and design shall be based on Section 301.1.4 regardless of which compliance method is used.
Exception: Subject to the approval of the code official, alterations complying with the laws in existence at the time the building or the affected portion of the building was built shall be considered in compliance with the provisions of this code unless the building is undergoing more than a limited structural alteration as defined in Section 907.4.4. New structural members added as part of the alteration shall comply with the International Building Code. Alterations of existing buildings in flood hazard areas shall comply with Section 701.3.
CHAPTER 3: COMPLIANCE

## Slide 13
301.1.1 Prescriptive compliance method. Repairs, alterations, additions and changes of occupancy complying with Chapter 4 of this code in buildings complying with the International Fire Code shall be considered in compliance with the provisions of this code.
301.1.2 Work area compliance method. Repairs, alterations, additions, changes in occupancy and relocated buildings complying with the applicable requirements of Chapters 5 through 13 of this code shall be considered in compliance with the provisions of this code.
301.1.3 Performance compliance method. Repairs, alterations, additions, changes in occupancy and relocated buildings complying with Chapter 14 of this code shall be considered in compliance with the provisions of this code.
CHAPTER 3: COMPLIANCE

## Slide 14: Prescriptive
Chapter 4:
4

## Slide 15: 401
401.1 Scope. The provisions of this chapter shall control the alteration, repair, addition and change of occupancy or relocation of existing buildings and structures, including historic buildings and structures as referenced in Section 301.1.1.
Exception: Existing bleachers, grandstands and folding and telescopic seating shall comply with ICC 300.
401.1.1 Compliance with other methods. Alterations, repairs, additions and changes of occupancy to or relocation of, existing buildings and structures shall comply with the provisions of this chapter or with one of the methods provided in Section 301.1.
CHAPTER 4: PRESCRIPTIVE

## Slide 16: 401
401.2 Building materials and systems. Building materials and systems shall comply with the requirements of this section.
401.2.1 Existing materials. Materials already in use in a building in compliance with requirements or approvals in effect at the time of their erection or installation shall be permitted to remain in use unless determined by the building official to be unsafe per Section 115.
401.2.2 New and replacement materials. Except as otherwise required or permitted by this code, materials permitted by the applicable code for new construction shall be used. Like materials shall be permitted for repairs and alterations, provided no hazard to life, health or property is created. Hazardous materials shall not be used where the code for new construction would not permit their use in buildings of similar occupancy, purpose and location.
CHAPTER 4: PRESCRIPTIVE

## Slide 17: 401
401.2.3 Existing seismic force-resisting systems. Where the existing seismic force-resisting system is a type that can be designated ordinary, values of R, Ω0 and Cd for the existing seismic force-resisting system shall be those specified by the International Building Code for an ordinary system unless it is demonstrated that the existing system will provide performance equivalent to that of a detailed, intermediate or special system.
401.3 Dangerous conditions. The building official shall have the authority to require the elimination of conditions deemed dangerous.
CHAPTER 4: PRESCRIPTIVE

## Slide 18: Section 402: Additions
402.1 General. Additions to any building or structure shall comply with the requirements of the International Building Code for new construction. Alterations to the existing building or structure shall be made to ensure that the existing building or structure together with the addition are no less conforming to the provisions of the International Building Code than the existing building or structure was prior to the addition. An existing building together with its additions shall comply with the height and area provisions of Chapter 5 of the International Building Code.
CHAPTER 4: PRESCRIPTIVE

## Slide 19: Section 403
403.1 General. Except as provided by Section 401.2 or this section, alterations to any building or structure shall comply with the requirements of the International Building Code for new construction. Alterations shall be such that the existing building or structure is no less conforming to the provisions of the International Building Code than the existing building or structure was prior to the alteration.
Exceptions:
1. An existing stairway shall not be required to comply with the requirements of Section 1011 of the International Building Code where the existing space and construction does not allow a reduction in pitch or slope.
2. Handrails otherwise required to comply with Section 1011.11 of the International Building Code shall not be required to comply with the requirements of Section 1014.6 of the International Building Code regarding full extension of the handrails where such extensions would be hazardous due to plan configuration.
CHAPTER 4: PRESCRIPTIVE

## Slide 20
403.3 Existing structural elements carrying gravity load. Any existing gravity load-carrying structural element for which an alteration causes an increase in design gravity load of more than 5 percent shall be strengthened, supplemented, replaced or otherwise altered as needed to carry the increased gravity load required by the International Building Code for new structures. Any existing gravity load-carrying structural element whose gravity load-carrying capacity is decreased as part of the alteration shall be shown to have the capacity to resist the applicable design gravity loads required by the International Building Code for new structures.
CHAPTER 4: PRESCRIPTIVE

## Slide 21
403.3.1 Design live load. Where the alteration does not result in increased design live load, existing gravity load-carrying structural elements shall be permitted to be evaluated and designed for live loads approved prior to the alteration. If the approved live load is less than that required by Section 1607 of the International Building Code, the area designed for the nonconforming live load shall be posted with placards of approved design indicating the approved live load. Where the alteration does result in increased design live load, the live load required by Section 1607 of the International Building Code shall be used.
403.10 Smoke alarms. Individual sleeping units and individual dwelling units in group R and I-1 occupancies shall be provided with smoke alarms in accordance with the Michigan building code. R 408.30565a
CHAPTER 4: PRESCRIPTIVE

## Slide 22: Section 404
404.1 General. Buildings and structures, and parts thereof, shall be repaired in compliance with Sections 401.2 and 404. Work on nondamaged components that is necessary for the required repair of damaged components shall be considered part of the repair and shall not be subject to the requirements for alterations in this chapter. Routine maintenance required by Section 401.2, ordinary repairs exempt from permit in accordance with Section 105.2, and abatement of wear due to normal service conditions shall not be subject to the requirements for repairs in this section.
CHAPTER 4: PRESCRIPTIVE

## Slide 23: Section 406
406.1 Replacement glass. The installation or replacement of glass shall be as required for new installations.
406.3 Replacement window emergency escape and rescue openings. Where windows are required to provide emergency escape and rescue openings in Group R-2 and R-3 occupancies, replacement windows shall be exempt from the requirements of Sections 1030.2, 1030.3 and 1030.5 of the International Building Code provided the replacement window meets the following conditions:
The replacement window is the manufacturer’s largest standard size window that will fit within the existing frame or existing rough opening. The replacement window shall be permitted to be of the same operating style as the existing window or a style that provides for an equal or greater window opening area than the existing window.
The replacement of the window is not part of a change of occupancy.
CHAPTER 4: PRESCRIPTIVE

## Slide 24: Section 407
407.1 Conformance. No change shall be made in the use or occupancy of any building unless such building is made to comply with the requirements of the International Building Code for the use or occupancy. Changes in use or occupancy in a building or portion thereof shall be such that the existing building is no less complying with the provisions of this code than the existing building or structure was prior to the change.
Subject to the approval of the building official, the use or occupancy of existing buildings shall be permitted to be changed and the building is allowed to be occupied for purposes in other groups without conforming to all of the requirements of this code for those groups, provided the new or proposed use is less hazardous, based on life and fire risk, than the existing use.
Exception: The building need not be made to comply with the seismic requirements for a new structure unless required by Section 407.4.
CHAPTER 4: PRESCRIPTIVE

## Slide 25: Section 407
407.2 Certificate of occupancy. A certificate of occupancy shall be issued where it has been determined that the requirements for the new occupancy classification have been met.
CHAPTER 4: PRESCRIPTIVE

## Slide 26: Section 410
410.1 Scope. A building, facility, or element that has a change in use group or occupancy load or alteration shall comply in accordance with the requirements of the utilization of public facilities by physically limited, 1966 PA 1, MCL 125.1351 to 125.1356 and the Michigan building code, R 408.30401 to R 408.30499. R 408.30561
CHAPTER 4: PRESCRIPTIVE

## Slide 27: Classification
Chapter 5:
5

## Slide 28: Section 501
501.1 Scope. The provisions of this chapter shall be used in conjunction with Chapters 6 through 13 and shall apply to the alteration, repair, addition and change of occupancy of existing structures, including historic and moved structures, as referenced in Section 301.1.2. The work performed on an existing building shall be classified in accordance with this chapter.
501.2 Work area. The work area, as defined in Chapter 2, shall be identified on the construction documents.
CHAPTER 5: CLASSIFICATION

## Slide 29
501.3. Smoke alarm locations in existing buildings constructed before November 6, 1974. Within each dwelling unit or sleeping unit, a single-station smoke alarm shall be installed in the following locations:
In each sleeping room or each area directly outside the sleeping room.
On each floor level including the basement level. For sleeping units with split levels and without an intervening door between the adjacent levels, a smoke alarm installed on the upper level shall suffice for the adjacent lower level provided that the lower level is less than 1 full story below the upper level.
CHAPTER 5: CLASSIFICATION

## Slide 30: Section 502
502.1 Scope. Repairs, as defined in Chapter 2, include the patching or restoration or replacement of damaged materials, elements, equipment or fixtures for the purpose of maintaining such components in good or sound condition with respect to existing loads or performance requirements.
CHAPTER 5: CLASSIFICATION

## Slide 31: Section 503
503.1 Scope. Level 1 alterations include the removal and replacement or the covering of existing materials, elements, equipment, or fixtures using new materials, elements, equipment, or fixtures that serve the same purpose.
503.2 Application. Level 1 alterations shall comply with the provisions of Chapter 7.
CHAPTER 5: CLASSIFICATION

## Slide 32: Section 504
504.1 Scope. Level 2 alterations include the reconfiguration of space, the addition or elimination of any door or window, the reconfiguration or extension of any system, or the installation of any additional equipment.
504.2 Application. Level 2 alterations shall comply with the provisions of Chapter 7 for Level 1 alterations as well as the provisions of Chapter 8.
CHAPTER 5: CLASSIFICATION

## Slide 33: Section 505
505.1 Scope. Level 3 alterations apply where the work area exceeds 50 percent of the building area.
505.2 Application. Level 3 alterations shall comply with the provisions of Chapters 7 and 8 for Level 1 and 2 alterations, respectively, as well as the provisions of Chapter 9.
CHAPTER 5: CLASSIFICATION

## Slide 34: Section 506
506.1 Scope. Change of occupancy provisions apply where the activity is classified as a change of occupancy as defined in Chapter 2.
506.2 Application. Changes of occupancy shall comply with the provisions of Chapter 10.
CHAPTER 5: CLASSIFICATION

## Slide 35: Repair
Chapter 6:
6

## Slide 36: Section 601
601.1 Scope. Repairs as described in Section 502 shall comply with the requirements of this chapter. Repairs to historic buildings need only comply with Chapter 12.
601.2 Conformance. The work shall not make the building less conforming than it was before the repair was undertaken.
CHAPTER 6: REPAIR

## Slide 37: Section 602: Building Elements and Materials
602.1 Existing building materials. Materials already in use in a building in compliance with requirements or approvals in effect at the time of their erection or installation shall be permitted to remain in use unless determined by the code official to render the building or structure unsafe or dangerous as defined in Chapter 2.
602.2 New and replacement materials. Except as otherwise required or permitted by this code, materials permitted by the applicable code for new construction shall be used. Like materials shall be permitted for repairs and alterations, provided no dangerous or unsafe condition, as defined in Chapter 2, is created. Hazardous materials, such as asbestos and lead-based paint, shall not be used where the code for new construction would not permit their use in buildings of similar occupancy, purpose and location.
CHAPTER 6: REPAIR

## Slide 38
602.3 Glazing in hazardous locations. Replacement glazing in hazardous locations shall comply with the safety glazing requirements of the International Building Code or International Residential Code as applicable.
Exception: Glass block walls, louvered windows, and jalousies repaired with like materials.
CHAPTER 6: REPAIR

## Slide 39: Section 603: Fire Protection
603.1 General. Repairs shall be done in a manner that maintains the level of fire protection provided.
CHAPTER 6: REPAIR

## Slide 40: Section 604: Means of Egress
604.1 General. Repairs shall be done in a manner that maintains the level of protection provided for the means of egress.
CHAPTER 6: REPAIR

## Slide 41: Section 607: Electrical
607.1 Material. Existing electrical wiring and equipment undergoing repair shall be allowed to be repaired or replaced with like material.
CHAPTER 6: REPAIR

## Slide 42: Section 608: Mechanical
608.1 General. Existing mechanical systems undergoing repair shall not make the building less conforming than it was before the repair was undertaken.
CHAPTER 6: REPAIR

## Slide 43: Section 609: Plumbing
609.1 Materials. Plumbing materials and supplies shall not be used for repairs that are prohibited in the International Plumbing Code.
CHAPTER 6: REPAIR

## Slide 44: Alteration Level 1
Chapter 7:
7

## Slide 45: Section701
701.1 Scope. Level 1 alterations as described in Section 503 shall comply with the requirements of this chapter. Level 1 alterations to historic buildings shall comply with this chapter, except as modified in Chapter 12.
CHAPTER 7: ALTERATION LEVEL 1

## Slide 46: Section 702:
702.1 Interior finishes. All newly installed interior wall and ceiling finishes shall comply with Chapter 8 of the International Building Code.
CHAPTER 7: ALTERATION LEVEL 1

## Slide 47
702.5 Emergency escape and rescue openings. Where windows are required to provide emergency escape and rescue openings in Group R-2 and R-3 occupancies and one and two-family dwellings and townhouses regulated by the International Residential Code, replacement windows shall be exempt from the requirements of Sections 1030.2, 1030.3 and 1030.5 of the International Building Code and Sections R310.21 and R310.2.3 of the International Residential Code accordingly, provided the replacement window is the manufacturer’s largest standard size window that will fit within the existing frame or existing rough opening. The replacement window shall be permitted to be of the same operating style as the existing window or a style that provides for an equal or greater window opening area than the existing window.
Window opening control devices complying with ASTM F 2090 shall be permitted for use on windows required to provide emergency escape and rescue openings.
CHAPTER 7: ALTERATION LEVEL 1

## Slide 48: Section 704:
704.1 General. Alterations shall be done in a manner that maintains the level of protection provided for the means of egress.
CHAPTER 7: ALTERATION LEVEL 1

## Slide 49: Section 706:
706.1 General. Materials and methods of application used for recovering or replacing an existing roof covering shall comply with the requirements of Chapter 15 of the International Building Code.
Exception: Reroofing shall not be required to meet the minimum design slope requirement of one-quarter unit vertical in 12 units horizontal (2-percent slope) in Section 1507 of the International Building Code for roofs that provide positive roof drainage.
CHAPTER 7: ALTERATION LEVEL 1

## Slide 50: Alteration Level 2
Chapter 8:
8

## Slide 51: Section 801:
801.1 Scope. Level 2 alterations as described in Section 504 shall comply with the requirements of this chapter.
Exception: Buildings in which the reconfiguration is exclusively the result of compliance with the accessibility requirements of Section 705.2 shall be permitted to comply with Chapter 7.
CHAPTER 8: ALTERATION LEVEL 2

## Slide 52: Section 804:
804.1 Scope. The requirements of this section shall be limited to work areas in which Level 2 alterations are being performed, and where specified they shall apply throughout the floor on which the work areas are located or otherwise beyond the work area.
CHAPTER 8: ALTERATION LEVEL 2

## Slide 53
804.4 Fire alarm and detection. An approved fire alarm system shall be installed in accordance with Sections 804.4.1 through 804.4.3. Where automatic sprinkler protection is provided in accordance with Section 804.2 and is connected to the building fire alarm system, automatic heat detection shall not be required.
An approved automatic fire detection system shall be installed in accordance with the provisions of this code and NFPA 72. Devices, combinations of devices, appliances, and equipment shall be approved. The automatic fire detectors shall be smoke detectors, except that an approved alternative type of detector shall be installed in spaces such as boiler rooms, where products of combustion are present during normal operation in sufficient quantity to actuate a smoke detector.
CHAPTER 8: ALTERATION LEVEL 2

## Slide 54: Section 805:
805.3.1 Minimum number. Every story utilized for human occupancy on which there is a work area that includes exits or corridors shared by more than one tenant within the work area shall be provided with the minimum number of exits based on the occupancy and the occupant load in accordance with the International Building Code. In addition, the exits shall comply with Sections 805.3.1.1 and 805.3.1.2.
CHAPTER 8: ALTERATION LEVEL 2

## Slide 55: 805
805.3.1.1 Single-exit buildings. Only one exit is required from buildings and spaces of the following occupancies:
In Group A, B, E, F, M, U and S occupancies, a single exit is permitted in the story at the level of exit discharge when the occupant load of the story does not exceed 50 and the exit access travel distance does not exceed 75 feet (22 860 mm).
Group B, F-2, and S-2 occupancies not more than two stories in height that are not greater than 3,500 square feet per floor (326 m2), when the exit access travel distance does not exceed 75 feet (22 860 mm). The minimum fire-resistance rating of the exit enclosure and of the opening protection shall be 1 hour.
Open parking structures where vehicles are mechanically parked.
In Group R-4 occupancies, the maximum occupant load excluding staff is 16.
CHAPTER 8: ALTERATION LEVEL 2

## Slide 56
Groups R-1 and R-2 not more than two stories in height, when there are not more than four dwelling units per floor and the exit access travel distance does not exceed 50 feet (15 240 mm). The minimum fire-resistance rating of the exit enclosure and of the opening protection shall be 1 hour.
In multilevel dwelling units in buildings of occupancy Group R-1 or R-2, an exit shall not be required from every level of the dwelling unit provided that one of the following conditions is met:
  6.1. The travel distance within the dwelling unit does not exceed 75 feet (22 860 mm); or 6.2. The building is not more than three stories in height and all third-floor space is part of one or more dwelling units located in part on the second floor; and no habitable room within any such dwelling unit shall have a travel distance that exceeds 50 feet (15 240 mm) from the outside of the habitable room entrance door to the inside of the entrance door to the dwelling unit.
CHAPTER 8: ALTERATION LEVEL 2

## Slide 57
In Group R-2, H-4, H-5 and I occupancies and in rooming houses and child care centers, a single exit is permitted in a one-story building with a maximum occupant load of 10 and the exit access travel distance does not exceed 75 feet (22 860 mm).
In buildings of Group R-2 occupancy that are equipped throughout with an automatic fire sprinkler system, a single exit shall be permitted from a basement or story below grade if every dwelling unit on that floor is equipped with an approved window providing a clear opening of at least 5 square feet (0.47 m2) in area, a minimum net clear opening of 24 inches (610 mm) in height and 20 inches (508 mm) in width, and a sill height of not more than 44 inches (1118 mm) above the finished floor.
CHAPTER 8: ALTERATION LEVEL 2

## Slide 58
In buildings of Group R-2 occupancy of any height with not more than four dwelling units per floor; with a smokeproof enclosure or outside stairway as an exit; and with such exit located within 20 feet (6096 mm) of travel to the entrance doors to all dwelling units served thereby.
In buildings of Group R-3 occupancy equipped throughout with an automatic fire sprinkler system, only one exit shall be required from basements or stories below grade.
CHAPTER 8: ALTERATION LEVEL 2

## Slide 59: 805
805.6 Dead-end corridors. Dead-end corridors in any work area shall not exceed 35 feet (10 670 mm).
Exceptions:
Where dead-end corridors of greater length are permitted by the International Building Code.
In other than Group A and H occupancies, the maximum length of an existing dead-end corridor shall be 50 feet (15 240 mm) in buildings equipped throughout with an automatic fire alarm system installed in accordance with the International Building Code.
In other than Group A and H occupancies, the maximum length of an existing dead-end corridor shall be 70 feet (21 356 mm) in buildings equipped throughout with an automatic sprinkler system installed in accordance with the International Building Code.
In other than Group A and H occupancies, the maximum length of an existing, newly constructed, or extended dead-end corridor shall not exceed 50 feet (15 240 mm) on floors equipped with an automatic sprinkler system installed in accordance with the International Building Code.
CHAPTER 8: ALTERATION LEVEL 2

## Slide 60: 806
806.1 General. A building, facility, or element that is altered shall comply with this section and Section 410. R 408.30577
808.1 New installations. All newly installed electrical equipment and wiring relating to work done in any work area shall comply with all applicable requirements of NFPA 70 except as provided for in Section 808.3.
CHAPTER 8: ALTERATION LEVEL 2

## Slide 61: 808
808.1 New installations. All newly installed electrical equipment and wiring relating to work done in any work area shall comply with all applicable requirements of NFPA 70 except as provided for in Section 808.3.
CHAPTER 8: ALTERATION LEVEL 2

## Slide 62: Alteration Level 3
Chapter 9:
9

## Slide 63: 901
901.1 Scope. Level 3 alterations as described in Section 505 shall comply with the requirements of this chapter.
901.2 Compliance. In addition to the provisions of this chapter, work shall comply with all of the requirements of Chapters 7 and 8. The requirements of Sections 803, 804 and 805 shall apply within all work areas whether or not they include exits and corridors shared by more than one tenant and regardless of the occupant load.
Exception: Buildings in which the reconfiguration of space affecting exits or shared egress access is exclusively the result of compliance with the accessibility requirements of Section 705.2 shall not be required to comply with this chapter.
CHAPTER 9: ALTERATION LEVEL 3

## Slide 64: 903
903.1 Existing shafts and vertical openings. Existing stairways that are part of the means of egress shall be enclosed in accordance with Section 803.2.1 from the highest work area floor to, and including, the level of exit discharge and all floors below.
904.1 Automatic sprinkler systems. An automatic sprinkler system shall be provided in a work area where required by Section 804.2 or this section.
905.1 General. The means of egress shall comply with the requirements of Section 805 except as specifically required in Sections 905.2 and 905.3.
CHAPTER 9: ALTERATION LEVEL 3

## Slide 65: 905
905.1 General. The means of egress shall comply with the requirements of Section 805 except as specifically required in Sections 905.2 and 905.3.
CHAPTER 9: ALTERATION LEVEL 3

## Slide 66: 904
904.1 Automatic sprinkler systems. An automatic sprinkler system shall be provided in a work area where required by Section 804.2 or this section.
905.1 General. The means of egress shall comply with the requirements of Section 805 except as specifically required in Sections 905.2 and 905.3.
CHAPTER 9: ALTERATION LEVEL 3

## Slide 67: Change in Occupancy
1
0
Chapter 10:

## Slide 68: 1001
1001.1 Scope. The provisions of this chapter shall apply where a change of occupancy occurs, as defined in Section 202.
1001.2 Certificate of occupancy. A change of occupancy or a change of occupancy within a space where there is a different fire protection system threshold requirement in Chapter 9 of the International Building Code shall not be made to any structure without the approval of the code official. A certificate of occupancy shall be issued where it has been determined that the requirements for the change of occupancy have been met.
CHAPTER 10: CHANGE IN OCCUPANCY

## Slide 69: 1001
1001.2.1 Change of use. Any work undertaken in connection with a change in use that does not involve a change of occupancy classification or a change to another group within an occupancy classification shall conform to the applicable requirements for the work as classified in Chapter 5 and to the requirements of Sections 1002 through 1011.
Exception: As modified in Section 1205 for historic buildings.
CHAPTER 10: CHANGE IN OCCUPANCY

## Slide 70: 1001
1001.2.2 Change of occupancy classification or group. Where the occupancy classification of a building changes, the provisions of Sections 1002 through 1012 shall apply. This includes a change of occupancy classification and a change to another group within an occupancy classification.
1001.3 Certificate of occupancy required. A certificate of occupancy shall be issued where a change of occupancy occurs that results in a different occupancy classification as determined by the International Building Code.
CHAPTER 10: CHANGE IN OCCUPANCY

## Slide 71: 1008
1008.2 Unsafe conditions. Where the occupancy of an existing building or part of an existing building is changed, all unsafe conditions shall be corrected without requiring that all parts of the electrical system comply with NFPA 70.
1012.1 General. The provisions of this section shall apply to buildings or portions thereof undergoing a change of occupancy classification. This includes a change of occupancy classification within a group as well as a change of occupancy classification from one group to a different group or where there is a change of occupancy within a space where there is a different fire protection system threshold requirement in Chapter 9 of the International Building Code. Such buildings shall also comply with Sections 1002 through 1011. The application of requirements for the change of occupancy shall be as set forth in Sections 1012.1.1 through 1012.1.4. A change of occupancy, as defined in Section 202, without a corresponding change of occupancy classification shall comply with Section 1001.2.
CHAPTER 10: CHANGE IN OCCUPANCY

## Slide 72: 1012
1012.1 General. The provisions of this section shall apply to buildings or portions thereof undergoing a change of occupancy classification. This includes a change of occupancy classification within a group as well as a change of occupancy classification from one group to a different group or where there is a change of occupancy within a space where there is a different fire protection system threshold requirement in Chapter 9 of the International Building Code. Such buildings shall also comply with Sections 1002 through 1011. The application of requirements for the change of occupancy shall be as set forth in Sections 1012.1.1 through 1012.1.4. A change of occupancy, as defined in Section 202, without a corresponding change of occupancy classification shall comply with Section 1001.2.
CHAPTER 10: CHANGE IN OCCUPANCY

## Slide 73: Addition
Chapter 11:
1
1

## Slide 74: 1101
1101.1 Scope. An addition to a building or structure shall comply with the International Codes as adopted for new construction without requiring the existing building or structure to comply with any requirements of those codes or of these provisions, except as required by this chapter. Where an addition impacts the existing building or structure, that portion shall comply with this code.
CHAPTER 11: ADDITION

## Slide 75: 1101
1101.2 Creation or extension of nonconformity. An addition shall not create or extend any nonconformity in the existing building to which the addition is being made with regard to accessibility, structural strength, fire safety, means of egress, or the capacity of mechanical, plumbing, or electrical systems.
1101.3 Other work. Any repair or alteration work within an existing building to which an addition is being made shall comply with the applicable requirements for the work as classified in Chapter 5.
CHAPTER 11: ADDITION

## Slide 76: 1103
1103.1 Compliance with the International Building Code. Additions to existing buildings or structures are new construction and shall comply with the International Building Code.
CHAPTER 11: ADDITION

## Slide 77: Questions?